Firmware outline for the Xmega-E5

Overview

Xmega-E5
Potentiometer to ADC
Gnd
DAC – Audio range
LED D100
LED D101
RS232 uC2Host
RS232 Host2uC
Vcc
Square wave
Button Sine or Triangle
# Xmega system requirements
## System
### Clock
System clock speed: 32MHz
System clock source: Internal oscillator
### Timer Counter
Timer period: 5ms
Timer result: Interrupt for programme updating
## Hardware inputs
### Button
Button push type: toggle
Button push pin setting: internal pull up
Button push pin interrupt: Falling edge
Button push pin debounce: yes – in firmware
### Potentiometer – ADC
#### Potentiometer
Potentiometer range: 0-10kΩ
Potentiometer type: Linear
#### ADC
ADC sample timing: predictable, set times
ADC filtering: Firmware LPF with alpha ~0.7 or internal averaging
ADC input: single ended
ADC gain: 1
ADC mode: Unsigned
ADC ref voltage: AVcc/2
ADC resolution: 12 bits
ADC channel: 0
### RS232
RS232 levels: 0v – 3v3
RS232 setup: 1 start, 1 stop, 8 bits, no parity
RS232 baud rate: 115200 fixed
RS232 input actions: not implemented, for future use
## Outputs
### DAC
DAC voltage reference: 3V3 on AVcc
DAC channel selection : single
DAC channel: 0
### Square wave output - PWM
Pin type: Waveform generation
Slope type: single
### RS232
RS232 levels: 0v – 3v3
RS232 setup: 1 start, 1 stop, 8 bits, no parity
RS232 baud rate: 115200 fixed
### LED outputs
LED on: pin low – current sink
LED off: Pin high impedance