Design outline for the Xmega-E5
The following lists the design requirements for the Xmega-E5 to be used as a variable frequency oscillator (VFO) for the synth. Output waveforms will be sine or triangle and square. The document consists of:
1. Xmega-E5 ADD
2. System Requirements
3. Xmega-E5 Pinouts

# Xmega-E5 ADD

Xmega-E5
Potentiometer to ADC
Gnd
DAC – Audio range
LED D100
LED D101
RS232 uC2Host
RS232 Host2uC
Vcc
Square wave
Button Sine or Triangle

Voltage translation
Square Wave
Square Wave

Filter
DAC output
Filtered DAC

# System requirements
UART speed: 57600 1 start, 1 stop, 8 data, no parity
UART protocol: RS232
UART Host2uC: Not currently implemented
UART uC2Host output:
Code debug information as necessary
ADC input read value
DAC output value
Vcc: 3v3
DAC output voltage: 1V pk-pk
DAC frequency range: 10Hz to 20kHz
DAC waveform: Sine or triangle wave
DAC filtering -6dB @ 30kHz??
DAC filter type: Sallen and Key
Rotary input: 4 states on 3 input pins
Rotary function: Switch between Sine, Triangle, Square and Square/2 waveforms
Square wave output duty cycle: Fixed 50/50
Square wave frequency range: same as DAC
Square wave output voltage: 0V or 3V3
Square wave peak voltage translation: 3V3 to 1V
Square wave voltage translation: resistor divider plus unity gain buffer
ADC input voltage range: 0 to AVcc/2
ADC potentiometer range: 0Ω to 10kΩ
0Ω -> 10Hz
10kΩ -> 20kHz
Timer counter period: 5ms
Timer counter output: interrupt
Timer counter port & pin: TC4
RTC: 5ms system wakeup
# Xmega-E5 Pin outs
Xmega-E5
Connector & pin	Port & Pin	Signal name	Comment
J2 - 1	PA0	ADC0	Input
J2-2	PA1	GPIO	Input for wave selector (SQ/2)
J2 – 3	PA2	DAC0	Output
J2 – 4	PA3	GPIO	Input for wave selector (SQ)
J2 – 5	PA4	GPIO	Input for wave selector (TRI)
J2 - 5	PD4	LED D100	Active Low
J2 - 8	PD5	LED D101	Active Low
J2 - 9	-	Gnd
J2 - 10	-	3V3
J4-5	PC4	PWM
SW0	PD0	Switch 0	Needs internal pullup